34

# Приложение № 4

(с корабля не выносить)

## Лоцманская карточка корабля

14

# Приложение № 4

(с корабля не выносить)

35

## Pilot list of  the ship

# Text boxes

30 град

38,2м

5.2м

163,5м

8.7м

16,5м

| Особенности управления | Маневренные элементы | Технические средства |
| --- | --- | --- |
|  | Скорость | Циркуляция | Навигация | Механизмы |
|  | Положение телеграфа | V, узл | Положение руля | V, узл | Rц, м | α, град/с |  |  |
| Vmin = 6 узл | вперед товсь | 4 | 10 | 6 |  |  | Навигационные РЛС – 2, гирокомпас, лаг, эхолот – в строю, поправки: * Δ ГК = 0,0 град; * Δ Нэ = - 1,5 м | Движители – 2 |
|  | вперед самый малый | 6 |  | 9 |  |  |  | N = 100 000 л.с. |
| t реверса = 15 с | вперед малый | 9 | 15 | 6 |  |  |  | Подруливающее |
|  | вперед средний | 14 |  | 9 |  |  |  | устройство - 2 |
| t начала циркуляции = 10 с | вперед полный | 18 | 25 | 6 |  |  |  | Якорное устройство – |
|  |  |  |  | 9 |  |  |  | 2 шпиля |

### Командир корабля:                         О. Будин

30 degr

38,2 m

5.2 m

163,5 m

8.7 m

16,5 m

| Control features | Maneuvering elements | Technical facilities |
| --- | --- | --- |
|  | Speed | Circulation | Navigation | Mechanisms |
|  | telegraph position | Speed knots | rudder position | Speed knots | R, m | α, degr/с |  |  |
| Speed min = 6 knots | stand by ahead | 4 | 10 | 6 |  |  | Radar’s – 2, gyrocompass, loq, echo sounder – in order, corrections: * Δ QC = 0,0 degr; * Δ Нes = - 1,5 m | Propulsiorns – 2 |
|  | dead slow ahead | 6 |  | 9 |  |  |  | N = 100 000 h.p. |
| reverse time = 15 sec | slow ahead | 9 | 15 | 6 |  |  |  | Thrusters - 2 |
|  | half ahead | 14 |  | 9 |  |  |  | Anchor |
| begining of circulation = 10 sec | full ahead | 18 | 25 | 6 |  |  |  | arrangement |
|  |  |  |  | 9 |  |  |  | 2 capstans |

### Skipper:                         О. Budin