Pls find NEW TURKISH STRAITS VESSEL TRAFFIC SERVICE USER'S GUIDE

Quote

ABBREVIATIONS

AIS : Automatic Identification System

CCTV : Closed Circuit Television

COLREG : Collision Regulations (International Regulations for Prevention of Collisions at

Sea)

DF : Direction Finder

DSC : Digital Selective Calling.

EC : European Community

ECDIS : Electronic Chart Display and Information System

ENC : Electronic Navigational Chart

ETA : Estimated Time of Arrival

IALA : International Association of Marine Aids to Navigation and

Lighthouse Authorities

IMO : International Maritime Organisation

IR : Infrared

MMSI : Maritime Mobile Service Identity

PPU : Portable Pilot Unit

RT : Radio Telephone

SMCP : Standard Marine Communication Phrases

SOLAS : International Convention for the Safety of Life at Sea 1972

SP : Sailing Plan

TSS : Traffic Separation Scheme

TSVTS : Turkish Straits Vessel Traffic Services

TUBRAP : Turkish Straits Reporting System

UTC : Universal Time Coordinated

VHF : Very High Frequency

VTS : Vessel Traffic Service

VTSC : Vessel Traffic Service Centre

WGS : World Geodetic System

GENERAL

Introduction

The Turkish Straits VTS has been established in accordance with applicable national laws

and international rules and regulations in order to improve the safety of navigation, protection

of life, environment, and property in the Turkish Straits by using the latest technology. This

User's Guide has been prepared to provide information related to the services provided,

needed by the participant vessels that are navigating in the Turkish Straits. This User's

Guide aims to be used together with the Turkish Straits Maritime Traffic Regulations, as

promulgated in the Official Gazette no.23515 of 6 November 1998.

Operation

The TSVTS shall be operated in accordance with the Turkish Straits Maritime Traffic

Regulations, as promulgated in the Official Gazette no.23515 of 6 November 1998 together

with the IMO Resolutions A.857 (20) and A.827 (19).

Competent Authority

Minister of Transport of the Republic of Turkey.

Administration

Undersecretariat for Maritime Affairs.

TSVTS Authority

The Director General for Coastal Safety and Salvage Administration.

Services Provided

The TSVTS, prepared taking into account related IALA resolutions and recommendations

and in compliance with IMO Resolutions A.857(20) and A.827(19) provides the Information

Service, Navigational Assistance Service and Traffic Organization Service.

Service Area

The TSVTS covers the area indicated in figures no. 1, 2, 3, 4, 5 and 6 (in the near future the

Marmara Sea area will also be covered so that the entire area of the Turkish Straits will be

included in the TSVTS service area).

Active Participant Vessel

Vessels carrying dangerous cargo and vessels 20 meters in length or over, whether in

stopover or non-stopover passage through the Turkish Straits, for whatever purpose, shall be

designated as "Active Participant" vessels within the TSVTS area and it is strongly

recommended that Active Participant vessels comply with all the requirements of TUBRAP.

Passive Participant Vessel

Vessels less than 20 meters in length and local traffic vessels within the TSVTS area, for

whatever purpose, shall be designated as "Passive Participant" vessels.

Passive participants are not required to participate in TUBRAP. However, VHF frequency of

the sector should be monitored at all times and all messages given by the TSVTS should be

followed within the TSVTS Area.

Caution

Within the TSVTS system, an ENC, prepared based upon WGS 84 datum, is in service.

Participants using charts of a different datum should make the necessary datum corrections

for the positions given by the TSVTS in latitudes and longitudes.

TURKISH STRAITS REPORTING SYSTEM

Traffic Separation Schemes

The limits of the traffic separation scheme for the Turkish Straits and their approaches, as

adopted by the IMO and as established in accordance with Rule 10 of the Convention on the

COLREG are provided below:

Northern Limits:                                     Southern Limits:

41o16´N/ 028o55´E                               40o 05´ N / 026o 11´ E

41o21´N/ 028o55´E                               40o 02´ N / 025o 55´ E

41o21´N/ 029o16´E                               39o 50´ N / 025o 53´ E

41o14´N/ 029o16´E                               39o 44´ N / 025o 55´ E

39o 44´ N / 026o 09´ E

SP 1 Report

Masters, owners or agents of the vessels carrying dangerous cargo or the vessels that are

500 GT and above should submit a written Sailing Plan 1(SP-1) to the VTS Centers at least

24 hours prior to entry into the Turkish Straits. Masters, owners or agents of the vessels that

are between 200-300m in length and/or vessels with a draft over 15m should submit a written

Sailing Plan 1(SP-1) at least 48 hours prior to entrance.

Owners or operators of vessels that are more than 300m in length; vessels that are propelled

by nuclear power; and vessels carrying nuclear cargo or nuclear waste provide information

regarding their characteristics and cargo to the Administration during the planning stage of

the voyage. The TSVTS and, if necessary the Administration, based upon the data provided

by such vessels, shall inform the relevant vessel's owner, operator or master, of the

requirements and recommendations, if any, necessary to ensure a safe passage of the

vessel through the Turkish Straits, taking into consideration all specifications of the vessels

including the dimensions and maneuvering capabilities, the morphological and physical

structure of the Turkish Straits, the condition of the season the navigation, safety of life,

property and environment as well as the maritime traffic; the subject matter vessels that

possess the necessary conditions for passage submit a SP 1 at least 72 hours in advance.

SP 1 REPORT FORM

Designator Information Required

A SHIP'S NAME, CALL SIGN, FLAG, IMO No, MMSI No  (Mobile Maritime Service Identification No)

B DATE AND TIME (UTC)

C REPORTING POSITION (LAT/LONG)

F CONTINUOUS MANOEUVRING SPEED (in knots including decimals)

G PORT OF DEPARTURE

H DATE, TIME AND POINT OF ENTRY INTO VTS AREA (UTC)  (Eta for Mehmetcık or Gelibolu Traffic Control)

I PORT OF DESTINATION

JREQUEST PILOT (YES/NO)

ISTANBUL STRAIT

MARMARA SEA

ÇANAKKALE STRAIT

O FORWARD AND AFT DRAFT, MAX AIR DRAFT (AT THE ENTERANCE)

P CARGO (TYPE AND QUANTITY)

Q DEFECTS/DAMAGE/DEFICIENCIES/OTHER LIMITATING REASONS

R DESCRIPTION OF DANGEROUS, NUCLEER AND POLLUTANT

GOODS(UN NO/NAME/CLASS/QUANTITY) *

T SHIP'S AGENT/REPRESANTATIVE TAX NO

U SHIP TYPE

LOA /BEAM (METRES)

GT / NRT

X P&I INFORMATION (P&I Club Name / Policy Number /Validity)

(*) Detailed information from the ship related with her cargo may be requested for

safety considerations.

Vessels carrying dangerous cargo and/or vessels 500 GT and above, about to depart from

ports in the Sea of Marmara, shall submit sailing plan SP 1 Report at least 6 hours prior to

their departure.

TUBRAP reports should be properly prepared and sent to the VTSC in a timely manner.

The SP 1 report is of great importance to efficient traffic management. As failure to

provide SP 1 report in a timely manner may cause delays, traffic congestion and

waiting, vessels that fail to comply may be excluded from the daily traffic plan.

SP 1 report should be sent to the addresses below.

For Istanbul;

· Fax: + 90 212 323 48 06

323 48 07

323 48 08

· Telex: 26699 VTCI

· INM-C: 492868022

· Delivery service/Hand over to the VTS Center

Address: Istanbul Bogazi Gemi Trafik Hizmetleri Merkezi

Istinye Cad. Eski Tersane içi

34460 Istinye/Istanbul

For Çanakkale;

Fax: + 90 286 2131240

2131241

2133077

Telex: 58104 VTCC

INM-C: 492868021

Delivery Service/Hand over to the VTS Center

Address: Çanakkale Bogazi Gemi Trafik Hizmetleri Merkezi Akbas Mevkii

17900 Eceabat/Çanakkale

SP 2 Report

Ship masters who reported that their vessels are technically suitable and who have already

submitted an SP 1 Report and masters or commanding officers of warships and state-owned

vessels not used for commercial purposes, submit an SP 2 Report that has been prepared 2

hours or 20 miles (whichever comes first) prior to entry into the Istanbul or Çanakkale Straits

to the TSVTS via the designated VHF/RT channel.

After having submitted the SP 2 Report, vessels shall proceed taking into account

information provided by the TSVTS and shall record in the ship's log all information provided

in the SP 2 Report and all information regarding traffic in the Turkish Straits.

The SP 2 report shall be submitted to the concerned sector of the TSVTS area where the

ship will enter into.

SP 2 REPORT FORM

Designator Information Required

A SHIP'S NAME, CALL SIGN, FLAG, IMO NO, MMSI NO

D SHIP'S POSITION (BEARING AND DISTANCE)

H DATE AND TIME OF ENTRY INTO THE TURKISH STRAITS

J REQUEST PILOT (YES OR NO)

ISTANBUL STRAIT

MARMARA SEA

ÇANAKKALE STRAIT

T SHIP'S AGENT / REPRESENTATIVE

Q DEFECTS/DAMAGE/DEFICIENCIES/OTHER LIMITATING REASONS

Reference points for position "D" :

Türkeli Lighthouse Position : 41° 14.10' N / 029° 06.70' E

Ahirkapi Lighthouse Position : 41° 00.40' N / 028° 59.20' E

Gelibolu Lighthouse Position : 40° 24.60' N / 027° 41.00' E

Mehmetçik Lighthouse Position : 40° 02.70' N / 026° 10.50' E

Position Report

Vessels 20 meters in length and over that will enter the Straits of Istanbul and Çanakkale,

when within 5 nautical miles from the entry to the Strait, shall provide a Position Report

containing information identifying themselves to the TSVTS sector at the entry.

POSITION REPORT FORM

Designator Information Required

A SHIP'S NAME

D POSITION

Call Point Report

Vessels 20 meters in length and over in passage through the Istanbul and Çanakkale Straits,

should provide the Call Point Report via VHF/RT, to the concerned TSVTS sector, at the

positions designated. These positions are the entry and exit points of the TSVTS.

Furthermore, vessels should provide this report via VHF/RT channel to the new sector at

each change of sector.

CALL POINT REPORT FORM

Designator Information Required

A SHIP'S NAME

D POSITION

COMMUNICATIONS

Communication Language and Format

· The communication language of the TSVTS being English, SMCP shall be employed in

order to ensure an accurate communication.

· Turkish vessels / Vessels employing pilots, may communicate in Turkish.

· The following message markers should be used for communications with the TSVTS.

When Communication used in Turkish

Language

· BILGI

· TAVSIYE

· UYARI

· TALIMAT

· SORU

· CEVAP

· TALEP

· NIYET

When Communication used in English

Language

· INFORMATION

· ADVICE

· WARNING

· INSTRUCTION

· QUESTION

· ANSWER

· REQUEST

· INTENTION

In circumstances deemed to be necessary, the TSVTS operator may repeat a message in

English to Turkish and/or vice-versa.

When communicating with the TSVTS care should be exercised not to speak rapidly and to

pronounce words correctly.

TSVTS shall operate in VHF/ RT channels 11, 12, 13 and 14.

"Except as related to safety of navigation all other communication on these channels

is forbidden."

The VTS operator of sector concerned is responsible for maintaining the proper

communication procedures on the VHF channel of his/her sector and has the duty to report

every misuse of the frequency to the Authorities.

VHF 06 will be used for emergencies.

VHF 67 has been designated for meteorological purposes. However may be used for making

general announcements by the TSVTS when needed.

In principle, while inside the TSVTS area and as far as is practicable, there should be no

communication between vessels; all communication shall be conducted through the TSVTS.

Working channels should not be used outside of the TSVTS purpose.

Keeping in mind that the system provides ships positions and records all communications, all

stations transmitting on VHF should refrain from unnecessary communications and maintain

at all times proper communication discipline.

Sectors and VHF channels

VTS Sector Limits

The sectors and corresponding VHF/RT working channels in the Istanbul Strait are in the

following order from north to south.

SECTOR NAME WORKING CHANNELS CALL SIGN

TÜRKELI VHF/RT CH 11 SECTOR TÜRKELI

KAVAK VHF/RT CH 12 SECTOR KAVAK

KANDILLI VHF/RT CH 13 SECTOR KANDILLI

KADIKÖY VHF/RT CH 14 SECTOR KADIKÖY

The northern limits of the Istanbul VTS are the line connecting the following positions.

A : 410 10.5' N / 0290 35' E

B : 410 32.5' N / 0290 35' E

C : 410 32.5' N / 0280 45' E

D : 410 19' N / 0280 45' E

The southern limits of the Istanbul VTS are the lines connecting the following positions.

A : 400 53.1' N / 0290 10.8' E

B : 400 52.4' N / 0290 08.2' E

C : 400 50.3' N / 0290 07.5' E

D : 400 45.2' N / 0290 07.4' E

E : 400 49.1' N / 0280 42.6' E

F : 400 57.3' N / 0280 37.5' E

The sectors and corresponding VHF/RT working channels in the Çanakkale Strait are in

following order from north to south.

SECTOR NAME WORKING CHANNEL CALL SIGN

GELIBOLU VHF/RT CH 11 SECTOR GELIBOLU

NARA VHF/RT CH 12 SECTOR NARA

KUMKALE VHF/RT CH 13 SECTOR KUMKALE

The northern limit of the Çanakkale VTS is a line joining the following positions.

A : 400 36.47' N / 0270 06.8' E

B : 400 26.65' N / 0270 06.8' E

The southern limit of the Çanakkale VTS is the line connecting the following positions and/or

following the shoreline.

A : 390 44' N / 0260 09.2' E

B : 390 44' N / 0250 55' E

C : 390 52.6' N / 0250 47' E

D : 400 06' N / 0250 47' E

E : 400 09' N / 0260 00.9' E

F : 400 09' N / 0260 14.2' E

Sector Gelibolu

The northern limit of this sector is the line joining the following positions.

A : 400 36.47' N / 0270 06.8' E

B : 400 26.65' N / 0270 06.8' E

The southern limit of this sector is the line joining the following positions.

A : 400 21.56' N / 0260 37.65' E

B : 400 20.15' N / 0260 39.75' E

Sector Nara

The northern limit is the same as the southern limit of sector Gelibolu.

The southern limit is the line joining the following positions.

A : 400 06.8' N / 026020.2 E

B : 400 05.7' N / 0260 21.75' E

Sector Kumkale

The northern limit is the same as the southern limit of sector in Nara.

The southern limit of this sector is the southern limit of the Çanakkale VTS.

Sector Türkeli

The northern limit of this sector is the northern limit of the Istanbul VTS.

The southern limit is the line joining Fil Burnu Light at (410 12.4' N / 290 07.13' E) and Çali

Burnu Light (410 12.43' N / 290 06.37' E)

Sector Kavak

The northern limit of this sector is the southern limit of sector Türkeli.

The southern limit is the Fatih Sultan Mehmet Bridge.

Sector Kandilli

The northern limit of this sector is Fatih Sultan Mehmet Bridge.

The southern limit of this sector is the line joining Haydarpasa Breakwater north end (410

00.6' N / 0290 00.1' E) and position ashore 410 00.6' N / 280 59.23' E including the Haydarpasa

Port and Kadiköy Breakwater

Sector Kadiköy

The northern limit of this sector is the southern limit of Sector Kandilli.

The southern limit of this sector is the southern limit of the Istanbul VTS.

SERVICES PROVIDED

Marine Traffic in the TSVTS delineated area is monitored by using Radar, ENC, AIS, CCTV

and VHF equipment such as VHF R/T, DSC and DF. TSVTS also receives information from

various sources on anticipated vessel movements, hazards to navigation, aids to navigation

and any other information of interests to TSVTS participants.

Information Service

· Marine Traffic information

· Information about the position of a vessel in relation with other vessels

· Information about positions of other vessels by means of distances from own vessel,

course and speed over the ground

· Information about intended movements of other vessels

· Notices to Mariners

· Hydrological information

· Meteorological information

· Information about the reported status of aids to navigation

· Any other information when deemed necessary by the TSVTS

Navigational Assistance Service

Navigational Assistance Service will be provided when severe meteorological situations have

been observed, deficiencies or breakdowns have occurred during the passage of the

participants, when required by the master or the person in charge or, when deemed

necessary by the TSVTS. With regard to the safety of navigation, decision making process

on the bridge of the participant vessels may be assisted by providing the following

information.

· Position information in order to ensure safe navigation of vessels sailing within the TSS

· Information about movements of other vessels in the vicinity

· Warnings with regard to dangerous situations that might develop

The beginning and ending time of the navigational assistance service must be clearly agreed

and recorded by the Master and TSVTS operator

Traffic Organization Service

This service is constituted from the following items:

· Vessel Sailing Plan and its entry permission, time and date to the Straits of Istanbul and

Çanakkale

· Any changes to the Sailing Plan

· Operational information before entering the Straits related to the traffic organization

· Operational information based upon the Turkish Straits Maritime Traffic Regulations

The SP 1 and SP 2 Reports constitute the primary sources for traffic organization service

provided by the TSVTS. Timely and accurate reporting of SP 1 and SP 2 will increase the

efficiency of traffic organization.

Vessels that do not provide correct and timely information will disrupt the orderly flow of

maritime traffic and may lead to delays as a result.

DEFINITIONS OF MAIN MESSAGE MARKERS USED BY THE VTS

Information: The TSVTS analyses the information collected from different sources and

distributes such data to participants according to their requests and needs. Information may

be given by the TSVTS at regular intervals or as requested by the participants or when

deemed necessary by the TSVTS. The purpose of informing participants is to facilitate the

safe navigation of vessels and to assist the ship masters in taking decisions.

Recommendation: TSVTS operators in charge, in order to prevent a potentially dangerous

situation or when deemed necessary, may make recommendations to all participant vessels

such as the taking of a pilot (for active participants only) or regarding maneuvers to be made.

Such recommendations do not relieve the master or person in charge of his or her

responsibility to navigate the vessel safely. Abiding by the recommendations is solely at the

initiative of the master or the person in charge. However it must be kept in mind at all times

that the Supervisors and the Operators of the TSVTS are former ocean-going shipmasters

who have been properly trained and licensed in accordance with IALA criteria.

Warning : TSVTS operators in charge will issue warnings to the participants when a

potentially dangerous situation occurs or is observed to be developing. TSVTS, after issuing

a warning, will monitor whether or not care had been exercised and action to prevent the

accident or dangerous situation had been taken.

Instruction: TSVTS may give instructions to all participant vessels upon the development of

an imminent and unavoidable danger, the violation of safety rules and regulations, when a

participant is not or does not seem to be aware of an imminent and obvious danger or in

case of a warning is ignored by a participant vessel.

Instructions given by the TSVTS shall always be result oriented, however all factors that

affect navigation, such as the steering or engine orders shall at all times remain with the

decision of those on board i.e. the master or pilot.

The TSVTS, while providing these services, shall at all times respect the master's ultimate

responsibility to control his/her vessel and shall exercise care not to interfere with the

traditional master-pilot relationship.

Taking into consideration that all decisions concerning the safe navigation of a vessel shall

be the sole responsibility of the master. Information, recommendations, warnings and

instructions provided by the TSVTS to the participants with regard to safety of navigation

shall at no time relieve the Master of his/her responsibility to manage his/her vessel and

possess the requisite knowledge and responsibility. The TSVTS shall at no time be held

responsible for decisions and actions taken by the Master.

PROCEDURES FOR SHIPS

In General

· Submission of SP 1 and SP 2 reports to the TSVTS in accordance with the Turkish

Straits Reporting system (TUBRAP).

· Call Point Reports shall be given during entry and exit of the TSVTS area and at the time

of changing sectors.

· VHF R/T channel of the TSVTS Sector shall be listened to at all times during passage or

anchorage when inside the TSVTS area.

· TSVTS should be informed at all times when vessels are leaving the TSVTS area.

· Vessels navigating within the Turkish Straits, for safety of navigation, protection of life

and of the environment, should continuously monitor all TSVTS broadcasts and take

heed of information, recommendations, warnings and instructions given by the TSVTS.

· Masters of vessels navigating within the Turkish Straits should report to the TSVTS all

perils to safety of navigation observed.

· Vessels navigating within the TSS through the Marmara Sea, whether in stopover or nonstopover

passage, in case of any deviation from the TSS, berthing or mooring to buoys,

dropping anchor, turning back or emergencies and similar exceptional circumstances and

any delays on their ETA's exceeding 2 hours should report to the concerned VTSC.

· Vessels engaging in non-stopover passage through the Turkish Straits should hoist the

signal flag "T" during the daytime and at night time exhibit a green light that can be

observed from all points in the horizon, both during passage or while at anchor.

· All communications concerned with pilotage service should be performed via VHF R/T

Channel 71.

For safety of navigation, protection of life and of the environment, pilotage is strongly

recommended to all vessels intending to engage in non-stopover passage through the

Turkish Straits.

Anchoring and Leaving the Anchorages

· Anchorage positions shall be determined by the TSVTS.

· Anchored vessels should report to the TSVTS their anchorage position and time.

· The concerned TSVTS sector channel should be continuously monitored at anchorage

areas.

· Vessels should inform the TSVTS one hour prior to heave up their anchors.

· When anchor has been heaved up, the vessel should notify the TSVTS of the time of

heaving up anchor, its port of destination and ETA, and obtain the necessary traffic

information.

· Vessels engaging in non-stopover passage through the Turkish Straits, with the

permission of the TSVTS, may anchor, up to 48 hours without having to obtain a "Free

Pratique".

Berthing and Unberthing

· Vessels after berthing should notify the TSVTS Center. While moored in a port, it shall

not be required to listen to the sector channel.

· Vessels should inform the TSVTS one hour prior to departing from the port and should

obtain permission for sailing from the TSVTS before single up.

· Vessels leaving the pier, prior to entering traffic, should report their time of departure as

well as ETA to the TSVTS, and proceed while receiving traffic information.

Slowing Down

Immediate notice should be given to the TSVTS Center when a vessel is forced to slow down

in either the Istanbul or Çanakkale Strait. The TSVTS Center shall assess the traffic situation

and provide information, recommendations and instructions regarding the situation.

Overtaking

Vessels shall not overtake another vessel unless there is an absolute necessity. In the case

of such necessity, a vessel intending to overtake another shall inform the TSVTS Center

prior to commencing the overtaking. The TSVTS Center shall assess the traffic situation and

provide information, recommendations and instructions regarding the situation. Effort shall be

made to overtake the vessel in a single maneuver.

However, overtaking shall not take place between Vaniköy and Kanlica in the Strait of

Istanbul and between Nara and Kilitbahir in the Strait of Çanakkale.

Reporting Accidents

Upon the occurrence of an accident inside the TSVTS area, both the vessel(s) involved in

the accident and the witnessing vessel(s) should immediately notify the TSVTS sector. The

TSVTS, is the first contact point for reporting accidents, so that the necessary precautions

can be taken to minimize any actual or potential casualties, loss of lives and property and for

the protection of the environment. The TSVTS will notify the appropriate authorities of such

reports or notices.

Reporting Incidents and Pollution

Vessels should immediately notify the TSVTS Center of any incident occurring within the

TSVTS that may interfere with the capability of vessels to safely maneuver or that creates a

danger to the marine environment or the surrounding areas, so that the necessary

precautions may be taken in a timely manner.

Local Traffic

Ferries, intra-city passenger vessels, fast ferries, passenger boats engaged in regular

voyages, pleasure crafts, fishing boats, agent boats, government vessels, tug boats, vessels

belonging to non-governmental organizations, vessels engage underwater operations and

survey vessels and all other similar vessels constitute local traffic.

Local traffic vessels, whether or not they are subject to SOLAS requirements, are under a

duty to monitor VHF R/T frequency and to follow the instructions issued by the TSVTS sector

in which they are located.

Local traffic vessels inside the Turkish Straits proceeding, according to COLREG, shall cross

the TSS by the shortest route available, keep out of the way of vessels navigating within the

TSS and not impede the passage of these ships.

Non-complying vessels should be reported to the TSVTS Center.

Sanitary Inspections

Vessels that will pass through the Turkish Straits shall be subject to Sanitary Inspections in

accordance with the 1936 Montreux Convention, at the positions as requested by the Turkish

Straits Maritime Regulations.

Bunker Vessels

Bunkering operations are carried out by informing the related TSVTS center and

independently of TSS.

· After getting alongside the vessel to be served, a report containing the following

information should be provided to the TSVTS Center:

- Name of the bunker vessel

- Name of the vessel being bunkered

- Time alongside

· After completion of bunkering operations a report containing the following information

should be provided to the TSVTS Center :

- Type and quantity of bunker supplied

- Cast off time

· TSVTS will add this information to the database

· TSVTS will inform vessels maneuvering in the area of the bunkering operations.

· Any leakage or spillage should be immediately reported to the TSVTS Center so that

the necessary precautions can be taken.

Fishing Boats

No fishing vessel, regardless of its length, may engage in any fishing activities while inside

the TSS. While outside of the TSS fishing vessels should maintain utmost care not to impede

the passage of other vessels.

Boats navigating by sail or oars

Navigating by sail or oars, swimming and hunting in the Turkish Straits TSS is prohibited.

However, sailing, rowing and swimming competitions conducted for sporting purposes, and

processions and special shows are subject to the permission and regulation of the

Administration.

Waste Collecting Vessels

Waste reception operations are carried out by informing the related TSVTS center and

independently of TSS.

· After getting alongside the vessel to be served, a report containing the following

information should be provided to the TSVTS Center:

- Name of the waste collecting vessel

- Name of the vessel being served

- Time of alongside

· After completion of the operations a report containing the following information should

be provided to the TSVTS :

- Type and quantity of waste collected

- Cast of time

· TSVTS will add this information to the database

· TSVTS will inform vessels maneuvering in the area of the waste collecting

operations.

· Any leakage or spillage should be immediately reported to the TSVTS Center so that

the necessary precautions can be taken.

Unquote

IMPORTANT

Dear master ;

Pls send SP1 report 24 hour ago enterence of the straits to our office by e-mail or fax msg.

Thanks/B.Rgds

Dursun Ayaz

Operation Department Assistant Manager

Anadolu Shipping Inc./ P&O Nedlloyd, Istanbul

Tel  :(+90) (0) 216 474 40 67 (pbx) / Ext nr. 131

Fax: (+90) (0) 216 474 51 12  -  474 38 42

E-Mail : d.ayaz@ponl.com